## Slide 1
Department of Electrical Engineering,
Sukkur IBA University
IoT Based Real Time Water Quality Monitoring System
Group Member:
Attiq ur Rehman
Muhammad Faizan
Project Advisor:
Dr. Safeer Hyder
Assistant Professor

## Slide 2: Problem Statement
The traditional system to determine water quality is not reliable.
It rely on collecting water samples, testing and analyses in water laboratories that is costly and time consuming.
Human errors can occur and may not provide accurate result.
It lack capability for real-time data capture, analyses and stakeholders can’t do fast dissemination on information for making timely and appropriate decisions.

## Slide 3
Designing a Real Time IoT Based Water Quality Monitoring System
An open-source system development of water monitoring
Reduce import cost
Improve local capacity building
Aims:
Objectives

## Slide 4: Proposed Solution
Designing a Real Time IoT Based Water Quality Monitoring System

## Slide 5
Maintain a continuous healthy water supply
Fish pond water quality testing
Industrial Waste Cleaning purpose
Applications

## Slide 6: What we have done so far?
Literature Review
Ignite Funding
Develop User Friendly Android App
Manage the Project on GitHub
Sensors Interfacing with Arduino/ESP8266
Data Visualization & Monitoring on Dashboard
Data Shifting to Cloud
IoT Platform Selection
Test sensors at Different Liquid samples
Email Alert

## Slide 7: pH Sensor Testing at different Liquids
Soap
Nestle
Milk Pack pH
pH Sensor
Nestle Pure
Water bottle PH
Hardware Connection
Standard Value

## Slide 8
pH ThingSpeak Dashboard
Gauge
Graph
Numeric Display
pH Sensor Values can be visualized and analyzed on the Thingspeak dashboard using graph, gauge & numeric display

## Slide 9
Android App
When pH Limit Exceeds then
we are generating the
email alert
Email Alert
The pH reading can be monitored using the light weight user friendly Android App
By Using App we can
Visualized
Analyzed
Monitored
Compare Results with Standard Predefined values

## Slide 10: TDS Sensor Testing at different Salt levels
TDS Result of
Drinking Water
TDS Result of
Salty Water
TDS Result of
Less Salty Water
TDS Sensor
Hardware Connection
TDS Standard Value

## Slide 11
ThingSpeak Dashboard
Graph
Numeric Display
Gauge
TDS sensor readings can be monitored and analyzed on the Thingspeak dashboard using graph, gauge & numeric display

## Slide 12
Android App Results & Email alert
When TDS Readings Exceeds
its Limit then we are generating
email alert
The TDS reading can be monitored using the light weight user friendly Android App
By Using App we can
Visualized
Analyzed
Monitored
Compare Results with Standard Predefined values

## Slide 13: Turbidity Sensor Testing at different Liquids
Dirty Water
Turbidity
Drinking Water
Turbidity
Parameter | WHO
Turbidity(NTU) | <5
Turbidity
Level
Turbidity
Level

## Slide 14
ThingSpeak Dashboard
Graph
Numeric Display
Gauge
Turbidity sensor readings can be monitored and analyzed on the Thingspeak dashboard using graph, gauge & numeric display

## Slide 15
Android App
The pH reading can be monitored using the light weight user friendly Android App
By Using App we can
Visualized
Analyzed
Monitored
Compare Results with Standard Predefined values

## Slide 16: Temperature sensor Interfacing
DS18B20 waterproof Temperature Sensor
Temperature of Drinking Water
Hardware Connection

## Slide 17
Temperature Sensor ThingSpeak Dashboard
Gauge
Graph
Numeric Display
Temperature Sensor Values can be visualized and analyzed on the Thingspeak dashboard using graph, gauge & numeric display

## Slide 18
Android App
The pH reading can be monitored using the light weight user friendly Android App
By Using App we can
Visualized
Analyzed
Monitored
Compare Results with Standard Predefined values

## Slide 19: Water Quality Test Results
Parameters | Standard value | Measured Value | Error | Accuracy
pH | 6.5-8.5 | 7.79 | 3.86% | 96.14%
Turbidity(NTU) | <5 | 5 | 4% | 96%
TDS(ppm) | <500(300 for Good Drinking water) | 394 | 23% | 77%
Standard Values: WHO Standard
Notes: Error= (Measured-real)/real x 100
Accuracy= 100- percentage error

## Slide 20: Android App

## Slide 21: Future Tasks:
User Friendly Dashboard
Develop Prototype & Chassis
Compare Results with IBA Water Supply System
Add the triggering functionality
Work at Sensors Calibration(Precision & Accuracy)
Thesis Manuscript
Thesis Submission

## Slide 22: Gantt Chart
Green: Completed task
Red: Future task

## Slide 23
https://ieeexplore.ieee.org/document/8821742
https://ieeexplore.ieee.org/abstract/document/9052289
https://ieeexplore.ieee.org/document/9117271
https://ieeexplore.ieee.org/abstract/document/9020583
https://ieeexplore.ieee.org/document/9242798
http://pep.ijieee.org.in/journal_pdf/11-247-146244659544-48.pdf
https://ijisrt.com/wp-content/uploads/2018/04/IoT-Based-Real-time-water-Monitoring-System-for-Smart-City.pdf
https://www.ripublication.com/awmc17/awmcv10n5_24.pdf
https://www.sciencedirect.com/science/article/pii/S1877050919309391
https://www.sciencedirect.com/science/article/pii/S2405844020309403
https://www.iotacommunications.com/blog/smart-water-quality-monitoring-system-using-iot/
References